## Slide 1: Reduced Order Modeling for CFD: Will Working in 3D eventually be Cheaper than Working in 2D? YES….

## Slide 2: Means for Design and Compliance Computational, Experimental, Flight Fluid Mechanics: CFD, EFD, FFD
CFD
1 day 5,000€
EFD
1 week
250,000€
FFD
1 month
$1,000,000€

## Slide 3: Reduced Order Modeling: the approach
“Provide a low-DoF approximation to the solution while retaining the same physics (RANS) and same dimensionality (3D)
Dramatic reduction in CPU time, from hours or days, to seconds
1. Sampling of the design space (DoE)
2. Obtain an set of snapshots of the system
3. Extract the “most energetic” modes from the ensemble (POD)
Off-line
4. Compute the solution of the system at “untried” conditions (Kriging)
On-line
Notes: specifies input parameters defining observation conditions, e.g. Mach, AoA for flow simulations; MVD, LWC for icing simulations. is the number of design variables.
are the snapshots defined with the input parameter . is the number of data point contained in a snapshot.
For CFD solutions, equals number of mesh nodes, for experimental data, equals number of probes.
can be pressure field, shear stress field, ice shape represented by the x, y, z coordinates, etc.
{𝐱_1,𝐱_2,…,𝐱_(𝑁_𝑆 ) } represent input parameters, e.g. Mach, AoA in flow simulations, MVD, LWC in icing simulations
{𝑼_1,𝑼_2,…,𝑼_(𝑁_𝑆 ) } are the snapshots defined with the input parameters, like pressure field (pressure values at mesh nodes), ice shape represented by the x, y, z coordinates

## Slide 4: ROM: The Successive Steps
DoE
Snapshots
POD
Kriging
Offline
Online
POD
Notes: POD yields a set of basis vectors that best represents the snapshots, according to the following maximization problem.
As a result, the problem of finding the functions can be recast as an eigenvalue-eigenvector problem, where 𝑅_𝑖𝑗 is a correlation matrix defined in terms of the scalar products between snapshots.

## Slide 5: Calculating the snapshots
Snapshots can be
  Numerical results
    Airflow solution
    Droplet solution
    Ice accretion solution
FLOW
ICE
DROP
Notes: The snapshots can be numerical results, experimental data, or even a combination of both, as long as they are dimensionally homogeneous, i.e. the same number of data points contained in each snapshot

## Slide 6: The physics of the problem are captured by the modes!
Ice thickness !
Upper horn !
Lower horn !
Modes 1 and 2
Mode 3
Mode 4
Modes 5, 6, etc.
do not add much
Notes: POD yields a set of basis vectors that best represents the snapshots, according to the following maximization problem.
As a result, the problem of finding the functions can be recast as an eigenvalue-eigenvector problem, where 𝑅_𝑖𝑗 is a correlation matrix defined in terms of the scalar products between snapshots.

## Slide 7: It Costs 5,000$ Per Hour to Run on 50,000 cores
That means 0.1$
per hour
per core

## Slide 8: How Many $ to Run 56 Snapshots?
Assuming 1 full day (24 hours) and 256 cores to run,
for a complete aircraft:
flow, impingement, accretion and performance degradation,
the cost of a ROM snapshot is less than 700$
Running 56 snapshots costs about 40,000$
That is less than the cost of one day in an icing tunnel !
and then you have a complete 3D icing simulator at your desk
At that point, 3D becomes cheaper than 2D!

## Slide 9: How Many Days to Run 56 Snapshots?
If each snapshot takes a full day?
And the answer is,
Still 1 Day!
50,000 cores / 256 cores = can easily run up to 195 snapshots simultaneously on same computer

## Slide 10: ROM applied to impingement

## Slide 11: ROM vs. full CFD: comparison of β
Comparison of collection efficiency at wing sections for CFD and ROM
60 seconds on 1 CPU
vs.
68 hours on 64 CPUs

## Slide 12: ROM vs. full CFD: comparison of β
Comparison of collection efficiency at pylon-nacelle for CFD and ROM

## Slide 13: ROM applied to ice accretion

## Slide 14: Aero-icing for DLR-F6 via ROM
Mesh 2,281,111 nodes, 1,875,932 tetra and 3,823,680 prisms (left).
Snapshots arrangement and target (red point) position (right)
Parameters: Mach, LWC (g/m3), time (s)
Data: Surface mesh after ice accretion
36 Snapshots have been used
AoA= 5o T=263 K MVD = 20 μm
Notes: Using POD/Kriging and 36 snapshots the ice shape can be accurately approximated (again just to stress that this specific ice shape does not come from snapshots, it is at uncalculated point). Minor traces can be seen. But the thickness of ice is insignificant.

## Slide 15: DLR-F6 – 3D Aero-icing, ice profile at selected cuts

## Slide 16: DLR-F6: ROM vs CFD
CFD
9 hours on 64 CPU (left)
ROM
25 s on 1 CPU (right)
Notes: Using POD/Kriging and 36 snapshots the ice shape can be accurately approximated (again just to stress that this specific ice shape does not come from snapshots, it is at uncalculated point). Minor traces can be seen. But the thickness of ice is insignificant.

## Slide 17: ROM applied to experimental measurements

## Slide 18: ROM with experimental data
ROM can be used as an aid to experimental campaigns where the measured data are used as snapshots
An experimental campaign in the IRT facility used 5 parameters: velocity, total temperature, LWC, MVD and spray time
to get 15 snapshots (upper figures)
The interested output is ice thickness at
locations E and F in the parameter space (right picture)

## Slide 19: ROM with experimental data, verification at target points
Ice thickness (left), experimental ice shape (right)
Rime ice
Glaze ice

## Slide 20: RBM with Experiments: Caradonna-Tung Test Case
RBM can be used in the context of experimental campaigns to reduce:
the complexity of the model
the number of tests to perform in the wind tunnel
Snapshots arrangement
Parameters of the analysis:
Pitch [degs]: 0 - 12
Rotational speed [rpm]: 650 – 2540
32 cond. x 5 sec. = 160 snapshots
Two-bladed rotor
NACA0012 airfoil
5 sections instrumented

## Slide 21: Reduction of Model Complexity
Model simplification: Reduction of model instrumentation to 3 sections instead of 5.
96 acquisitions instead of 160
Two targets have been chosen for validation:
 | r/R | ω [rpm] | α [deg]
Target A | 0.68, 0.89 | 1250 | 8
Target B | 0.68, 0.89 | 2268 | 5
A
B
Model simplification. Targets arrangement

## Slide 22: Model Simplification: Validation

## Slide 23: Model Simplification and Reduction of Tests
Reduction of tunnel tests: 3 sections and avoid all runs with Pitch = 8 deg
63 acquisitions instead of 160
Two targets are chosen for validation:
 | r/R | ω [rpm] | α [deg]
Target C | 0.68, 0.89 | 1250 | 8
Target D | 0.68, 0.89 | 2400 | 8
C
D
Reduction of tunnel tests
Targets arrangement

## Slide 24: Reduction of Model Complexity and Tunnel Tests: Validation

## Slide 25: ROM applied to CG calculation

## Slide 26: DLR-F6 – Change of CG, parametric analysis
Snapshots &
300 targets (left)
Weight increase (right)
CG variation (bottom)

## Slide 27: ROM applied to entire Appendix C for ice accretion and for aerodynamic performance 2D example

## Slide 28: ROM: Appendix C “Complete” Investigation of 2D Ice Shapes
30 snapshots selected via Centroidal Voronoi Tessellation
Parameters: LWC(g/m3), MVD (μm)
Desired output: Mass of ice
Angle of attack = 2.5 deg, Mach = 0.3
Altitude = 11000 ft., Time of accretion = 7 min.
GLC305 airfoil

## Slide 29: Exploration of App C for an airfoil
Notes: Two types of snapshots are considered: shape of ice and the associated & Cl-alpha curves
Leave-one-out of the first sampling iteration, with 56 snapshots

## Slide 30: ROM: Appendix C “Complete” Investigation Ice Shapes

## Slide 31: ROM applied to entire Appendix C for natural icing campaign 3D complete aircraft example

## Slide 32: Ice accretion after 25 min hold in stratiform clouds
MVD = 18.01 µm LWC = 0.40 g/m3 Temperature = 8.37 ̊ F

## Slide 33: LOOCV of the Initial Sampling
Altitude: 16,404 ft Speed: 268 KTAS AoA: 3.7° Exposure time: 25 minutes
Notes: Emphasize tat it is the first time that icing is calculated in 3D over the entre airplane, not just components

## Slide 34: Complete exploration of CM
Each ROM: 2 s on 16 CPUs
Mass of ice -- 25 min hold
1000 ROM solutions
LOOCV error -- ice thickness
103 snapshots
Each CFD-ICE: 16-32 h on 128 CPUs
Notes: At the end of the iterative sampling, 103 snapshots are obtained, partitioned into 3 clusters, for a final state of three local reduced-order bases.
Figure (left) shows the ice thickness error distribution for the last iteration. The maximum error has been reduced to 2.7 mm (which accounts for 9% of ), a 40% deduction of the maximum error obtained from the initial sampling, whereas for the majority of the icing envelope, the error is less than 1.2 mm.
At the end of the iterative sampling, 103 snapshots are obtained, partitioned into 3 clusters, for a final state of three local reduced-order bases.
Figure (left) shows the ice thickness error distribution for the last iteration. The maximum error has been reduced to 2.7 mm (which accounts for 9% of 𝛿_(𝑖𝑐𝑒,𝐶𝐹𝐷,𝑚𝑎𝑥)), a 40% deduction of the maximum error obtained from the initial sampling, whereas for the majority of the icing envelope, the error is less than 1.2 mm.

## Slide 35: Initial sampling and shape of ice used for aerodynamic degradation analysis
Notes: The ice shape considered is obtained by FENSAP-ICE from a 45-minute (1 shot) exposure under a CM icing condition (MVD = 21.26 μm, LWC = 0.30 g/m3), at typical holding flight conditions (5,000 meters pressure altitude, 268 knots true air speed and 3.675° AoA), with clean aircraft configuration (flaps/slats retracted, no deflection of control surfaces).
For the aerodynamic analysis in question, the snapshots are the flow variables of interest: pressure at the 9,788,214 nodes of the volume mesh and shear stress at the 202,260 surface nodes.
The ice shape considered is obtained by FENSAP-ICE from a 45-minute exposure under a CM icing condition (MVD = 21.26 μm, LWC = 0.30 g/m3), at typical holding flight conditions (5,000 meters pressure altitude, 268 knots true air speed and 3.675° AoA), with clean aircraft configuration (flaps/slats retracted, no deflection of control surfaces).
For the aerodynamic analysis in question, the snapshots 𝑼_𝑖 are the flow variables of interest: pressure at the 9,788,214 nodes of the volume mesh and shear stress at the 202,260 surface nodes.

## Slide 36: LOOCV error of the initial sampling, iced geometry
Max error 1.5%
Avg. error 0.17%
Max error 8.6%
Avg. error 1.7%
84 snapshots
Notes: volume weighted L2 norm error

## Slide 37: LOOCV error of the final sampling, iced geometry
Max error 1.3%
Avg. error 0.13%
Max error 6.0%
Avg. error 1.5%
129 snapshots
Notes: After seven sampling iterations, 129 snapshots were defined, with LOOCV error reduced to 1.3% and 6.0%, for pressure and shear stress, respectively

## Slide 38: LOOCV error of the final sampling, clean geometry
Max error 1.0%
Avg. error 0.14%
Max error 11.9%
Avg. error 3.5%
129 snapshots
Notes: In order to assess the aerodynamic performance degradation, flow solutions over the clean geometry are needed and 129 such snapshots under the same flight conditions as the ice-contaminated aircraft have been computed.

## Slide 39: ROM applied to a go-around scenario

## Slide 40: Flight path simulating an aborted landing
Each CFD:
21 h on 128 CPUs
Each ROM:
28 s on 16 CPUs
Notes: A hypothetical flight path representing an aborted descent is simulated using 21 target points, as shown in the top left figure.
Targets 1 to 9 represent the process that the airplane is allowed to exit holding pattern and descend to 3,000 feet; targets 9 to 13 demonstrate the abortion of the descend, where the AoA increases from 0.9° to 7.0°, and the airplane starts to regain altitude; targets 13 to 21 illustrate the climb stage, for which the aircraft gets back to the holding altitude and resume level flight AoA, after which it may need to prepare for a second landing, or fly to an alternate airport.
The ROM contains 4 solution fields, i.e. pressure and the x, y, z shear stress. The computation of each ROM takes 28 s using 16 CPUs, however, 87% of time is consumed in data reading, due to the limit of network band width. The actual computational time was only 3.6 s.

## Slide 41: ROM vs. CFD, iced geometry, target 13
Notes: Wing root

## Slide 42: ROM vs. CFD, iced geometry, target 13
Notes: Wing mid

## Slide 43: ROM vs. CFD, iced geometry, target 13
Notes: Wing tip

## Slide 44: ROM vs. CFD, iced geometry, target 13
Notes: Tail mid section

## Slide 45: Aerodynamic degradations in , and
Information developed in this research may be incorporated into a flight simulator.
Improve simulator fidelity and enable pilot training for in-flight icing

## Slide 46: Performance penalty for ice contaminated airplane
17% CL loss
60% CD increase
20% CM change

## Slide 47: ROM applied to desk or flight simulators

## Slide 48: Reduced Order Modeling’s objectives
Reduced Order Modeling (ROM):
  Provide an approach to considerably reduce cost of 3D simulations
  Provide a methodology to couple CFD, EFD and FFD data
  Provide a methodology to obtain information on APP C points not found in nature, giving a more complete picture of the icing and flight envelopes interaction
  Provide real-time representations of in-flight icing for pilot training